## Slide 1
Digital System Design Lab
Project: Design, Simulation & Implementation of Arithmetic & Logic Unit
Question
Solution
Equation
Design
Circuit
Team

## Slide 2
Question
Solution
Equation
Design
Circuit
Team
Design a 4 bit ALU using 4 bit full adder and also implement the “Carry”, “Overflow”, “Sign” and “Zero” flags. The ALU has two control signals (S1 & S0 ), two 4 bit input (A & B), a single bit Carry in ( Cin) and should output a 4 bit result and 4 flags. The ALU should perform according to the following:
S1 | S0 | Cin | Output | Explanation
0 | 0 | X | A⊕B | Logical “XOR” of A & B
0 | 1 | X | A’ | Logical “NOT” of A & B
1 | 0 | 0 | A+1 | Increment A
1 | 0 | 1 | A | Transfer A
1 | 1 | 0 | A+B+1 | Sum A & B with Carry
1 | 1 | 1 | A+B | Sum A & B

## Slide 3
Question
Solution
Equation
Design
Circuit
Team
S1 | S0 | Cin | Output | Explanation | X | Y | Z
0 | 0 | X | A⊕B | Logical “XOR” of A & B | A⊕B | 0 | 0
0 | 1 | X | A’ | Logical “NOT” of A & B | A’ | 0 | 0
1 | 0 | 0 | A+1 | Increment A | A | 0 | 1
1 | 0 | 1 | A | Transfer A | A | 0 | 0
1 | 1 | 0 | A+B+1 | Sum A & B with Carry | A | B | 1
1 | 1 | 1 | A+B | Sum A & B | A | B | 0
Solution Table

## Slide 4
Question
Solution
Equation
Design
Circuit
Team
The following equations are derived from the table which will help us design & implement the ALU.
X= S1 A + S1 ‘ ( S0 ‘ (A⊕B)+ S0 A’)
Y= S1 S0 B
Z= S1 Cin Cin

## Slide 5
Question
Solution
Equation
Design
Circuit
Team
Design and Simulation on Proteus

## Slide 6
Question
Solution
Equation
Design
Circuit
Team
The implemented circuit

## Slide 7
Question
Solution
Equation
Design
Circuit
Team
Raihan Tanvir
Humaira Ferdous Shifa
Ridwan Masud Khan